STRUTS AND TIES

An understanding of the terms, ‘struts, and ‘ties’ is important,. You should have an understanding of tensile, compressive and shear forces (see previous sheet). The part of the structure that has tensile force acting on it is called a TIE and the part that has compressive force acting on it is called a STRUT.

WALL

The beam is held in position by a steel rod. The weight of the beam is stretching the rod (tensile force).

ROOF

The roof beams are under pressure from the weight of the tiles on the roof (compressive force).The floor beam is being stretched (tensile force).

FLAGPOLE

The wires on either side of the flagpole are being stretched (tensile force).

Why is the pole under a compressive force?