Tutorial 4: 3D Geometry and Mesh Generation

________________________________________________

Introduction

This hands-on session illustrates the creation and mesh generation for relatively simple geometries in 3D with minimal instruction.

Example #1

- Create a face from a loop of straight edges that connect, in order, the points: (0,0), (1,0), (1.3,1), and (0.3,1).

- Sweep this face 1 unit in the z-direction to create a volume.

- Mesh the volume with the Map scheme using a spacing of 0.2.

Example #2

- Create a 2 x 2 x 2 brick (volume primitive) and a 10 x 10 x 10 brick using the direction of "+X+Y+Z" for both.

- Subtract the smaller brick from the larger one.

- Mesh the volume with the Submap scheme using a spacing of 1.0.

Example #3

- Create a sphere of radius 1.0 and a 2 x 2 x 2 brick with the direction of "+X+Y+Z."

- Intersect the two volumes.

- Mesh the volume with the Tet-Primitive scheme using a spacing of 0.2.

Example #4

- Create a 10 x 10 x 10 brick with the direction of "+X+Y+Z."

- Create a cylinder with a height of 10 and a radius of 2 with the direction of "z-axis."

- Move the cylinder with a displacement of (4,4,7).

- Rotate the cylinder about the x-axis by 20 degrees.

- Unite the volumes.

- Mesh the volume with the Cooper scheme using a spacing of 0.8.

- Remesh the volume with the Tet: TGrid scheme using the same spacing.  Compare the mesh sizes.